Uniform fibre bragg gratings :

- uniform FBG arrays have typical lengths up to 5 mm, and the minimum distance between each sensing element is usually limited to 10 mm
- Uniform FBGs are based on a periodical modulation of the refractive index in the core of an optical fiber , and they are the most popular grating-based type of technology.
- FBG sensors find current application in healthcare and medical devices, structural engineering , oil and gas , harsh environments, monitoring in nuclear plants, high temperature sensors

Chirped fibre bragg gratings:

- The CFBG on the other hand can be described as a semi-distributed sensor: it has an active length like a uniform FBG where the variation of strain or temperature is detectable, but within this region it can spatially resolve the temperature or strain profiles, like distributed sensors.
- CFBG sensors can use the same interrogation system as uniform FBGs, without requiring a complex and bulky interferometer.
- CFBGs have typical lengths of 15–50 mm and potentially can discriminate spatial events with millimeter resolution
- Most significantly, the key characteristic of the CFBG, in comparison with the uniform FBG, is the fact that the overall spectrum depends not only on the strain or temperature applied on the whole grating length, but rather on the temperature/strain recorded in each section of the grating
- CFBG can detect localized events, such as temperature hot spots or strain discontinuities, besides detecting the values of such parameters
- CFBGs became popular mainly for optical communications, as they enable dispersion compensation by means of introducing a differential group delay dependent on wavelength
- The reflected wavelength changes with the grating period, broadening the reflected spectrum.
- A grating possessing a chirp has the property of adding dispersion—namely, different wavelengths reflected from the grating will be subject to different delays.
- This property has been used in the development of phased-array antenna systems and polarization mode dispersion compensation, as well.

Tilted Fibre bragg Gratings:

- The tilted FBG is a new kind of sensor that includes all the advantages of established usage Bragg grating technology in addition to being able to excite cladding modes resonantly.
- This device opens possibilities for single-point sensing in hard-to-reach places
- TFBG sensors are using for mechanical and biochemical applications, including one-dimensional TFBG vibroscopes, accelerometers, and micro-displacement sensors; two-dimensional TFBG vector vibroscopes and vector rotation sensors; reflective TFBG refractometers with in-fiber and fiber-to-fiber configurations; polarimetric and plasmonic tilted FBG biochemical sensors for in-situ detection of a cell, protein, and glucose.

Super-structure fibre bragg gratings :

A superstructure fiber Bragg grating (SFBG), also called a sampled fiber Bragg grating, is a special FBG that consists of several small FBGs placed in close proximity to one another.
SFBGs have attracted attention in recent years with the discovery of techniques allowing the creation of equivalent chirp or equivalent phase shifts.

Advantages :

- can discriminate strain and temperature variations on the same grating
- The biggest advantage of an SFBG with the equivalent chirp or equivalent phase shifts is the possibility to generate gratings with a greatly fluctuating phase and amplitude by adjusting the spatial profile of the superstructure.
- The realization of SFBGs with the equivalent chirp or equivalent phase shifts requires only sub-millimeter precision.
- This technique permits to fabricate of long SFBGs with short phase masks
- Superstructure fiber Bragg grating is a novel fiber Bragg grating. Because it is flexible, passive, low insertion loss, and small polarization dependent. It causes great interest and enthusiasm for the people in many areas